## Slide 1: 01 Pendahuluan
Bayu Setiaji, M.Kom
ST151

## Slide 2: Pengenalan

## Slide 3: Alat Praktikum
Utama
Arduino: Uno / Nano / Mega
Breadboard
Kabel jumper
Arduino IDE
Piranti pendukung
Output: LCD, 7 Segment, LED, Buzzer
Input: sensor-sensor, button
Simulator: Tinkercad, Wokwi

## Slide 4: Arduino Boards
Mega
Uno
Nano

## Slide 5: Arduino Mega

## Slide 6: Arduino Uno
https://store.arduino.cc/collections/uno/products/arduino-uno-rev3

## Slide 7: Arduino Nano
https://store.arduino.cc/products/arduino-nano

## Slide 8: Pin
Sebagai pintu sambungan dengan peralatan lain
Dapat dikonfigurasi sebagai input dan output
Jenis:
  Digital
  Analog

## Slide 9: Contoh: Nano Pin

## Slide 10: Breadboard
Breadboard: papan sirkuit prototipe
Jalur koneksi

## Slide 11: Arduino IDE
Verify
Upload
Board Active
Sketchbook
Board Manager
Library Manager
Code Editor
Output
Serial Monitor
2
1
3
4
5
6
7
8
9

## Slide 12: Struktur Kode
void setup() {
// put your setup code here, to run once:
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 13: Hello World: menyalakan built-in LED
// Hello Arduino
const int pinLed = 13; // built-in LED
void setup() {
// put your setup code here, to run once:
pinMode(pinLed, OUTPUT); // set pinLed mode OUTPUT
}
void loop() {
// put your main code here, to run repeatedly:
digitalWrite(pinLed, HIGH); // Menyalakan LED
delay(1000); // delay 1000ms
}
Langkah
Klik tombol Verify
Amati layar Output, pastikan tidak ada error.
Klik tombol Upload
Amati LED di board akan menyala

## Slide 14: Flip Flop
Tambahkan kode seperti pada contoh yang di-highlite, kemudian Jalankan
Ubah nilai delay untuk mempercepat atau memperlambat kedipan
void loop() {
// put your main code here, to run repeatedly:
digitalWrite(pinLed, HIGH); // Menyalakan LED
delay(1000); // delay 1000ms
digitalWrite(pinLed, LOW); // mematikan LED
delay(1000);
}

## Slide 15: Mari merangkai…

## Slide 16
Selamat mencoba